## Slide 1: Environmental Impact of Electric Vehicles
Kristen Diedrich
March 12, 2012

## Slide 2: Outline
Perception of electric vehicles
Types of electric vehicles
Comparison of environmental impact
Cost Comparison
Possible future improvements

## Slide 3: How environmentally friendly are electric cars?

## Slide 4: Articles about Electric Cars
“Why Electric Vehicles Will Reduce Greenhouse Gas Emissions”
-Renewable Energy World
“Electric Cars Hold Greater Promise for Reducing Emissions and Lowering US Oil Imports, Study Finds”
-Science Daily
“Do Electric Cars Really Produce Fewer Emissions?”
-The Guardian
“Electric Vehicles Losing Their ‘Zero Emissions’ Claim in U.S.”
-Inside Climate News
“Electric Car Use May Increase Carbon Emissions”
-Energy Boom

## Slide 5: Zero Emissions?
Nissan Leaf Commercial:
http://www.youtube.com/watch?v=BhSqI77aLHU
Zero-Emissions Vehicle
  “Vehicles which produce no emissions from the on-board source of power”
  -California Air Resources Board
  What is the problem with this definition?
  How do we calculate “actual” emissions?

## Slide 6: Types of Electric Vehicles
Hybrid Electric Vehicle (HEV)
Plug-in Hybrid Electric Vehicle (PHEV)
Plug-in Electric Vehicle (PEV or EV)

## Slide 7: Method for Comparison
Calculate the CO2 Emissions of both a gas powered car and an electric car
Assumptions:
  Electric Car: Nissan Leaf
  Gas Car: generic car with average gas mileage

## Slide 8: Manufacturing-Related Emissions
Gas Powered Vehicle:
12,000 lbs CO2 per car
Electric Vehicle:
28,000 lbs CO2 per car
Main difference: internal combustion engine vs. lithium ion battery

## Slide 9: Gas Powered Vehicle Emissions
Assume:
19.4 lbs CO2 per gallon of gasoline
22.4 miles per gallon

## Slide 10: Electricity Sources
Coal | 44.9%
Natural Gas | 23.4%
Nuclear | 20.3%
Hydroelectric | 6.9%
Other | 4.5%
Emissions:
Coal: 2.17 lbs CO2 per kWh produced
Natural Gas: 1.40 lbs CO2 per kWh produced
Assume zero emissions for other sources
Average US CO2 emissions from electricity:
(2.17)(0.449) + (1.4)(0.234) = 1.30 lbs CO2 per kWh produced

## Slide 11: Electric Vehicle Emissions
Assume:
34 kWh per 100 miles
80% Efficiency
(34 kWh)/0.80 = 42.5 kWh needed to travel 100 miles

## Slide 12
Breakeven point: 51,000 miles driven

## Slide 13: What if…
All of your electricity comes from coal?
  2.17 lbs CO2 per kWh produced
  0.922 lbs CO2 per mile driven
  Remember, gas powered cars produce 0.866 lbs CO2 per mile driven
  In this situation, gas powered vehicles have a smaller carbon footprint than electric vehicles

## Slide 14: What if…
50% of your electricity is from renewable resources?
  33% from coal, 17% from national gas
  0.954 lbs CO2 per kWh produced
  0.405 lbs CO2 per mile driven
  Breakeven point with gas powered vehicles: 35,000 miles driven

## Slide 15: What if…
You live in Wisconsin?
  63% from coal, 9% from natural gas
  1.49 lbs CO2 per kWh produced
  0.635 lbs CO2 per mile driven
  Breakeven point with gas powered vehicles: 69,000 miles driven

## Slide 16: Economic Analysis
54% of people are willing to consider buying an electric vehicle
Only 9% willing to pay more than $2,000 extra for an EV
Current cost for a Nissan Leaf: $35,200
Average cost of a new car: $29,000

## Slide 17: Fuel Cost Comparison
Average Gas Price: $3.80 per gallon
Average Electricity Price: $0.12 per kWh

## Slide 18
Breakeven Point: 52,000 miles driven

## Slide 19: Possible Future Advances
Improve battery technology
  Increase battery life
  Increase range per charge
  Decrease emissions from manufacturing process
Decrease CO2 emissions from electricity
  Increase usage of nuclear and renewable fuels
  Clean Coal?
    Very politically-charged topic
Other ideas?

## Slide 20: Questions?